## Slide 1
GRIDLAB-D Simulation
Output_Message_Creation()
Multispeak
GetLatestReadings
Message Encoder
Multispeak
ODEventNotification
Message Encoder
Multispeak
Meter Disconnect
Message Encoder
DNP3 Value Status Message Encoder
DNP3 Voltage Control Message
DNP3 Switch Status Control Message
Packet Writer
File
Pcap File Writer
Packet Replay (Future)
SIMBA
Simulation Configuration File
A
B
C
D
E
F
GridLab-D Output .csv files
GridLab-D Model Input & Simulation Configuration Files
Input_Message_Creation()

## Slide 2
Message Creation Code & Logic Task List:
Verify GridLab-D model file provided by PNNL. [2 Days]. [9/22 – With modifications, the model now runs (with a sig. # of violations)]
  Model file consists of 1 substation and 5 feeders. The substation consists of two transformers and 23 switches. The feeders are various taxonomic feeders selected by PNNL and have approximately 1000 to 1500 individual meters each.
  Verify and/or collect reasonable input data for the GridLab-D simulation (i.e. load profiles sufficient to run at least a 1 month simulation)
Verify GridLab-D API [2 Days] [9/22 – New architecture proposed that does not require iterations with GridLab-D]
  Confirm ability to:
    Read system state variables (including power, energy, voltage values at meters and substation transformers and binary switch status
    Write system state variables (including substation switch status and meter connection status
    Iterate with successive GridLab-D simulations in a continuous fashion (each simulation run will be 4s in duration).
Write script to automate process of importing simulation configuration data, running GridLab-D, retrieving state information, performing simple calculations on state data (e.g. Is power > XXXX kW), and writing setpoint changes based on calculations [2 Days]
Write script to output message contents to a file. (The file format will be determined with help from the message creation team members. Message contents to be specified by message creation team members.) [2 Days]
Determine high level logic for the generation of messages (3 MultiSpeak message types & 3 DNP3 message types) [1 Day]
  Determine the data from GridLab-D required to evaluate the need for a message
  Determine the data from GridLab-D required to generate a message
  Determine the thresholds and/or message creation probabilities that are needed to generate messages
  Determine what configuration information is needed to run simulations with and without specified attacks
  [9/22 High level logic for simulation configuration, message creation, and attacks created. Default probabilities specified.]
Implement and test the logic for creating messages and writing messages to output file. [0.5 days / message type = 3 Days]
Generate simulated test data and train team members on use of the simulation system [2 Days]
Total Estimated Time Required: 14 Days – 3 Weeks
Desired Start: Monday, September 25 (End: Friday, October 13)

## Slide 3
1. Create a list of MultiSpeak and DNP3 payload structures and elements based on known network traffic/protocols. [2hrs - deliverable Friday 9/22]
2. Provide a mapping of the protocol elements to the GridState data dictionary. [2hrs - deliverable Friday 9/22]
3. For each of the payloads provide a script that reads the structured file from “Message and Creation Code & Logic” (purple block)
[20hrs - deliverable TBD coordinated with Bob W. Potential: Wednesday 9/27]
4. Script will have a time function for playback with a minimum time (fastest) that won’t overload the L2 JSON rest service. [Included above]
5. Encode the structured file event content into JSON messages to post to L2. [Included above]
6. Logging. [Included above]
7. Code for PCAP ‘ingest’ using live capture or replay for the other messages. This code will entail the parsing of the additional MultiSpeak and DNP3 messages. We have two working, and the models should suffice to define the build. It is an effort but straight forward.
Needs a final estimate and availability from Bob W. (I’m estimating 24hrs of the 40-60 estimate in ‘Resources’ below.
8. Code the “Packet Writer”. (This is Bob’s area.). The MultiSpeak is html to a fake html endpoint which we have a framework that was operational in May. The DNP3 doesn’t exist but I’ve tested some initial Git src and it may provide a good launch point for Bob after his evaluation.
Needs a final estimate and availability from Bob W. (Estimating 36hrs of the 40-60 estimate in ‘Resources’ below.
Resources:
1. Bob W. For some hours (full time not really needed I don’t think) from Monday through his return Oct 9th or so. For 1-6 above.
2. Resources post Oct 9th when we can get Bob W. Full time, or nearly so. (At least 30hr/wk) through Nov. I’d like him FT he provides additional contributions that are valuable.
#1-6 I think would be 20hrs.
#7 needs Bob’s input but I’ll ‘guess’ 40-60 based on his performance to date (but let him weigh in!)
#8 needs Bob’s input. It just has to be good enough to match the fields we need, plus pass the TCP stack. I have an example that may help I described above.
P.S., Had a conversation with Bob W. Told him about above guesses. He didn’t freak out :) but also needs time to think about it on his own. #5 is an easier lift than is #7, than is #8. #5 would enable us to process flat files asap. The other two are unnecessary for this but #7 needs to be done to read PCAP, and obviously #8 needs to be complete for ‘us’ to build PCAP.
Phil’s Tasks

## Slide 4: Older Versions

## Slide 5
SIMBA Simulation Configuration File
The SIMBA Input configuration file provides three types of information:
Message Creation Thresholds:
  Vmin, Vmax, Pmin, Pmax – These values are used by Output_Message_Creation() to determine if/when individual AMI meters should generate ODEventNotification (alarm) messages (Message Type B).
Message Transmission Probabilities:
  A: PMeterValue-Request PMeterValue-Respond – These probabilities determine whether correct Request and Respond messages are generated at each appropriate timestep (15 minutes) for meter values. (Output_Message_Creation() will generate message reading request and response messages with these probabilities. Meters may send values even when a request message is not generated (corresponding to messages that we fail to capture) [ Default Values: 1]
  B: PMeterEventSend – This probability is used by Output_Message_Creation() to determine whether a correct ODEventNotification message is sent by a meter when one of the message creation thresholds is triggered. [Default Value: 1]
  C: PMeterDisconnect-Trigger PMeterDisconnect-Request PMeterDisconnect-Action: These probabilities are used by Input_Message_Creation() to determine whether a Meter Disconnect action is requested by the control center at each timestep (this is implemented periodically on a coarse time step, say every 5 minutes), whether a meter disconnect message is generated, and whether the requested meter actually disconnects. (Note: The Meter Disconnect Trigger is evaluated first. If/when the Meter Disconnect Trigger is activated, then the other two probabilities are used to determine whether a message is generated and whether the meter disconnects. The meter may disconnect even if no meter disconnect message is generated (indicating that we missed the message in our capture device). [Default Values: 0]
  D: PDNP3Value-Request PDNP3Value-Response - These probabilities determine whether correct Request and Respond messages are generated at each appropriate timestep (4 seconds) for substation values. (Output_Message_Creation() will generate message reading request and response messages with these probabilities [ Default Values: 1]
  E: PVoltageControl-Send PVoltageControl-Action– The timestamp for all voltage control messages is pre-specified below. These probabilities are used to determine whether a message requesting the voltage control action is sent and whether the voltage control action is implemented. (The action can be taken even if the message is not generated and vice versa (corresponding to messages that we fail to capture.) [Default Values: 1]
  F: PSwitchControl-Send PSwitchControl-Action– The timestamp for all switch control (reconfiguration) messages is pre-specified below. These probabilities are used to determine whether a message requesting a switch status change is sent and whether the switch control action is implemented. (The action can be taken even if the message is not generated and vice versa (corresponding to messages that we fail to capture.) [Default Values: 1]
(continued on next slide)

## Slide 6
SIMBA Simulation Configuration File (Continued)
The SIMBA Input configuration file provides three types of information:
Pre-Specified Event Messages (Input_Message_Creation() is responsible for inserting each of the actions below into the GridLab-D model and generating the appropriate messages (subject to the probabilities specified above).
  VoltageControlActions: A list of voltage control actions (LTC tap changes or capacitor bank status changes) will be specified in the configuration file. Each item in the list will include a timestamp , a device identifier, and a setpoint.
    Note: Generally the voltage control actions should only be specified during low or high voltage conditions in the network. Therefore, it may be necessary to first run GridLab-D without any voltage control actions. The results from that first run can then be used to (manually) generate a list of voltage control actions to include in the simulation
  SwitchStatusActions: A list of switch status changes will be specified in the configuration file. Each item in the list will include a timestamp, a device identifier, and the action (OPEN/CLOSE).
Attacks
  AMI.1: Authorized Employee Issues Unauthorized Mass Remote Disconnect
    For this attack type, a list of meters and timestamps will be provided. At the given timestamps Input_Message_Creation() will trigger meter disconnects for all meters on the list. (Note: The creation of these messages and the likelihood of the disconnect will be subject to the PMeterDisconnect-Request PMeterDisconnect-Action probabilities only.)
  AMI.8: False Meter Alarms Overwhelm AMI and Mask Real Alarms
    For this attack type, a list of meters and timestamp will be provided. At the given timestamp Input_Message_Creation() will create ODEventNotification (alarm) messages for all specified meters.
  DGM.6: Spoofed Substation Field Devices Influence Automated Responses
    For this attack type, Output_Message_Creation() will artificially modify the connectivity, power or voltage status/readings at specified devices. A list of spoofed devices will be provided for this attack. Each item in the list will include a start and end timestamps, a device identifier, a quantity identifier (connection status, power, voltage), and a code indicating the change that should be calculated. (The “codes” will indicate whether a value should be reduced to 0, multiplied by a factor, set to a specific value, etc. [The ”codes” are to be determined.] Note: The creation of these spoofed messages does not change anything about how the GridLab-D simulation is run.
  DGM.10: Switched Capacitor Banks are Manipulated to Degrade Power Quality
    For this attack type, a list of substation devices and timestamps will be provided. At the given timestamp Input_Message_Creation() will trigger substation voltage or switch control messages for specified device(s). (Note: The creation of these messages and the likelihood of their implementation will be subject to the PVoltageControl-Send PVoltageControl-Action and PSwitchControl-Send PSwitchControl-Action probabilities.)
  Denial of Service Attack:
    For this attack type, a list of devices with start and end timestamps will be provided. Between the start and end timestamps all messages from the specified devices will not be created.

## Slide 7
GRIDLAB-D Simulation
(Runs for 4s and pauses)
GLM Model
System State
(Controls and Status)
Reports Completion of Simulation
Message Creation Code & Logic
Queries for System State
Sends updated control setpoints (switch status, LTC position, and meter connection status status
Multispeak
GetLatestReadings
Message Encoder
Multispeak
ODEventNotification
Message Encoder
Multispeak
Meter Disconnect
Message Encoder
DNP3 Value Status Message Encoder
DNP3 Voltage Control Message
DNP3 Switch Status Control Message
Packet Writer
Triggers 4s Simulation Continuation
Bob
Phil
Tim
File
Pcap File Writer
Packet Replay (Future)
SIMBA
Simulation Configuration File
A
B
C
D
E
F
Note: GridLab-D may not be capable of reporting simulation completions. A hardcoded time delay may be required.

## Slide 8
Message Creation Code & Logic Overview:
Collects and analyzes state data from GridLab-D to determine what messages need to be created.
Meter energy reads and voltage values are communicated after every 15 minutes
Substation switch status and power readings are communicated every 4 seconds (every simulation iteration).
AMI Event Notifications are sent only when voltage or power at AMI meters is beyond a predetermined threshold. (Successful message creation is determined by a specified probability.)
AMI Meter Disconnect messages are generated at each iteration with a specified probability. Disconnected meters are reconnected at each iteration with a specified probability.
DNP3 Voltage Control Messages are issued with some probability and/or delay when substation voltages are observed outside of specified bounds.
DNP3 switch status control messages are generated based on input configuration file.
INPUT configuration file may specify specific messages to send at specified timestamps (i.e. simulation attacks are speciifed as anomalous messages and/or anomalous control commands with a specific timestamp provided.
The Message creation code will write an output file with all the information required to generate messages. (The exact format is still to be designed. However, it is likely that every row in the output file would correspond to a unique message.). The Message Creation Code & Logic will only interact with GridLab-D in real-time. The code will have no direct interactions with the message and/or packet writing software.
Initially this code can run on a local machine. Running this in AWS may be required to run longer, more sophisticated simulation runs (with larger power system models).

## Slide 9
Message Creation Code & Logic Task List (DRAFT):
Verify GridLab-D model file provided by PNNL. [2 Days]
  Model file consists of 1 substation and 5 feeders. The substation consists of two transformers and 23 switches. The feeders are various taxonomic feeders selected by PNNL and have approximately 1000 to 1500 individual meters each.
  Verify and/or collect reasonable input data for the GridLab-D simulation (i.e. load profiles sufficient to run at least a 1 month simulation)
Verify GridLab-D API [2 Days]
  Confirm ability to:
    Read system state variables (including power, energy, voltage values at meters and substation transformers and binary switch status
    Write system state variables (including substation switch status and meter connection status
    Iterate with successive GridLab-D simulations in a continuous fashion (each simulation run will be 4s in duration).
Write script to automate process of importing simulation configuration data, running GridLab-D, retrieving state information, performing simple calculations on state data (e.g. Is power > XXXX kW), and writing setpoint changes based on calculations [2 Days]
Write script to output message contents to a file. (The file format will be determined with help from the message creation team members. Message contents to be specified by message creation team members.) [2 Days]
Determine high level logic for the generation of messages (3 MultiSpeak message types & 3 DNP3 message types) [1 Day]
  Determine the data from GridLab-D required to evaluate the need for a message
  Determine the data from GridLab-D required to generate a message
  Determine the thresholds and/or message creation probabilities that are needed to generate messages
  Determine what configuration information is needed to run simulations with and without specified attacks
Implement and test the logic for creating messages and writing messages to output file. [0.5 days / message type = 3 Days]
Generate simulated test data and train team members on use of the simulation system [2 Days]
Total Estimated Time Required: 14 Days – 3 Weeks
Desired Start: Monday, September 25 (End: Friday, October 13)

## Slide 10
Simulation
Timestamp
Should a message with meter interval reads be generated? (Has 15 minutes elapsed since last meter read message?)
Yes
No
Probability of successful message generation and transmission.
Substation Switch Status
Substation Transformer Status
(Power and Voltage Readings)
Should substation SCADA message be generated?
(Has 4 seconds elapsed since last meter read message?)
No Action
P
Write meter reading message contents to file.
1- P
No Action
Yes
No
Probability of successful message generation and transmission.
No Action
P
Write SCADA status message contents to file.
1- P
No Action
Meter Connect/Disconnect Message Probabilities
For every meter decide whether a meter connect or disconnect message should be generated
P
1- P
Write meter connect/disconnect message contents to file.
No Action
Update Meter Connection Status in GridLab-D
AMI Meter Status
(Connect, kWh, V)
For every meter decide whether a meter alarm message should be generated (compare values against thresholds)
Meter Alarm
Thresholds
Yes
No
Probability of successful message generation and transmission.
No Action
P
1- P
No Action
Write meter alarm message contents to file.
Example Message Creation Logic (INCOMPLETE DRAFT):
(No attack logic included)
C
B
A
D

## Slide 11
Substation Transformer Status
(=Voltage Readings)
Should any substation SCADA voltage control messages be generated?
(Compare voltage values against specified thresholds.)
Yes
No
Probability of operator action and message transmission to control voltage
No Action
P
Write SCADA voltage control message contents to file.
1- P
No Action
Switch reconfiguration Probabilities
For every switch decide whether a switch status change message should be generated.
P
1- P
Write switch status change control message contents to file.
No Action
Update Switch Status in GridLab-D
Example Message Creation Logic (INCOMPLETE DRAFT):
(No attack logic included)
F
E
Substation voltage control thresholds and probabilities